## Slide 1: Functional Safety of Automotive Operating Systems: An Overview
Junjie Mao
Tsinghua University
December 12, 2017

## Slide 2: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 3: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 4: Why functional safety?
Rather than thinking of the vehicle as a mechanical machine, with some electrical components, it would be more accurate to think of the vehicle as a distributed computer system programmed for personal transport.
Roger Rivett, “The Challenge of Technological Change in the Automotive Industry”, in C.Dale and T. Anderson (eds.), Achieving Systems Safety: Proceedings of the Twentieth Safety-Critical Systems Symposium, Bristol, UK, 7-9th February 2012, London: Springer-Verlag London Limited, 2012, p. 35.

## Slide 5: Why functional safety?
Yukihide Niimi, Takayuki Ono, Soichiro Arai Hideki sugimoto, and Riccardo Mariani, "Virtualization Technology and Using Virtual CPU in the Context of ISO26262: The E-Gas Case Study"

## Slide 6: Functional Safety: the Standards
IEC 61508:2010: Functional Safety of Electrical/Electronic/Programmable Electronic Safety-related Systems
  ISO 26262:2011: Road vehicles
  EN 50129: Railway
  IEC/EN 62061 & ISO 13849:2015: machinery
  IEC 60601: medical electrical equipment

## Slide 7: Functional Safety: the Standards
IEC 61508:2010: Functional Safety of Electrical/Electronic/Programmable Electronic Safety-related Systems
  ISO 26262:2011: Road vehicles
  EN 50129: Railway
  IEC/EN 62061 & ISO 13849:2015: machinery
  IEC 60601: medical electrical equipment

## Slide 8: Item Dissolution
System
Item
Source: ISO 26262-10:2012, p.4-5
Component
Notes: Source
- ISO 26262-10:2012, Clause 4.2

## Slide 9: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 10: Functional Safety: the Definition
absence of unreasonable risk due to hazards caused by malfunctioning behavior of E/E systems (ISO 26262-1:2011, 1.51)

## Slide 11: Functional Safety: the Definition
absence of unreasonable risk due to hazards caused by malfunctioning behavior of E/E systems (ISO 26262-1:2011, 1.51)
Extent of harm to person health that is unacceptable in a certain context

## Slide 12: Functional Safety: the Definition
absence of unreasonable risk due to hazards caused by malfunctioning behavior of E/E systems (ISO 26262-1:2011, 1.51)
electrical and/or electronic systems
  software + hardware

## Slide 13: Functional Safety: the Definition
absence of unreasonable risk due to hazards caused by malfunctioning behavior of E/E systems (ISO 26262-1:2011, 1.51)
in scope
System failure
Unintended behavior
not (directly) in scope
Functionality
Electric shock, fire, etc.
Security properties

## Slide 14: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 15: Faults, Errors, Failures and Hazards
Fault
Programming error at loop termination condition
Error
Unwanted endless loop (leads to watchdog-reset)
Failure
Engine control unit stops operation by intermittence
Error
Ignition interrupted by intermittence
Failure
Vehicle bucks
Fault
Engine control unit stops operation by intermittence
Item - Vehicle
Component - Engine Control Unit
Accident
Also called a hazard if it contributes to any accident scenario
Notes: Source:
- ISO 26262-10:2012, Clause 4.3

## Slide 16: Categorization of Failures
Failures
Single-point
Multiple-point
Dependent
Systematic
Random
SW
HW
HW
Common cause
Cascading
Safety Analysis
Safety mechanisms
Analysis on dependent failures
Notes: Source:
- ISO 26262-10:2012, Clause 4.3

## Slide 17: Safety Analysis
Given some known fault models, safety analyses
  examine the consequences of failures,
  find new hazards not previously identified, and
  Derive measures to prevent or mitigate violations.
Applied at either system, hardware or software level.
Methods
  Deductive: FTA, reliability block diagrams, Ishikawa diagram
  Inductive: FMEA, ETA, Markov modelling
Notes: Source:
- ISO 26262-9:2011, Clause 8

## Slide 18: Safety Mechanisms
Technical solutions to detect faults or control failures in a limited time interval.
Either
  switch to or maintain the item in a safe state, or
  alert the driver
Examples
  Hardware redundancy
  Parity bits and EDE codes for memory
  Software self-tests and watchdogs
Notes: Source:
- ISO 26262-4:2011, Clause 6

## Slide 19: Analysis of Dependent Failures
For each potential dependent failures identified by the safety analyses,
  determine if it is plausible, and
  specify measures for avoiding or controlling plausible dependent failures.
Applied either at system, hardware or software level.
Methods for identifying dependent failures
  Cut sets or repeated identical events of an FTA
  Repeated similar failure modes in an FMEA
Notes: Source:
- ISO 26262-9:2011, Clause 7

## Slide 20: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 21
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 22
Item Level
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 23
System Level
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 24
HW/SW Level
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 25
Requirement Phases
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 26
Design Phases
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 27
Test Phases
Notes: Source:
- ISO 26262-10:2012, Clause 7

## Slide 28: Requirement Phase Verification
Verify that the requirements comply with those they are derived from.
  (External) Consistency
  Correctness
  Completeness
Applied either at system, hardware or software level.
Methods
  Inspection or walkthrough
  Semi-formal or formal verification
Notes: Source:
- ISO 26262-8:2011, Clause 6

## Slide 29: Design Phase Verification
Verify that the design is compliant with the requirements.
  (External) Consistency
  Correctness
  Completeness
Applied either at system, hardware or software level.
Methods
  Inspection or walkthrough
  Simulation or prototyping
Notes: Source:
- ISO 26262-8:2011, Clause 9

## Slide 30: Test Phase Verification
Verify the products comply with their requirements by execution within a test environment.
Software unit/integration test methods
  Requirement-based, interface, fault-injection, resource usage, etc.
  Test cases derived from requirements
  Structural coverage should be determined
System integrate test methods
  Also include stress, long-term and user tests.
Notes: Source:
- ISO 26262-6:2011, Clause 9
- ISO 26262-6:2011, Clause 10
- ISO 26262-4:2011, Clause 8

## Slide 31: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 32: Automotive Safety Integrity Level
Hazardous event:
  an operational situation a hazard
For each hazardous event, classify its:
  Severity of harm: S0 S3
  Probability: E0 E4
  Controllability: C0 C3
  ASIL (Automotive Safety Integrity Level):
  QM A D
Notes: Source:
- ISO 26262-3:2011, Clause 7.4.3

## Slide 33: Requirements at Different ASIL
 | ASIL |  |  | 
 | A | B | C | D
Avoidance of undetected multi-point faults | + | + | +++ | +++
Modular system design | + | + | +++ | +++
Fault metrics for the final evaluation |  | + | +++ | +++
HW-SW interface testing with appropriate cov. |  |  | +++ | +++
Software partitioning is supported by HW |  |  |  | +++
Error handling mechanisms at SW arch. Level | + | + | +++ | +++
Structural coverage at SW arch. level | + | + | +++ | +++
 | ASIL |  |  | 
 | A | B | C | D
Avoidance of undetected multi-point faults | + | + | +++ | +++
Modular system design | + | + | +++ | +++
Fault metrics for the final evaluation |  | + | +++ | +++
HW-SW interface testing with appropriate cov. |  |  | +++ | +++
Software partitioning is supported by HW |  |  |  | +++
Error handling mechanisms at SW arch. Level | + | + | +++ | +++
Structural coverage at SW arch. level | + | + | +++ | +++
 | Neutral | + | Recommended
 |  | +++ | Required
 | Neutral | + | Recommended
 |  | +++ | Required
Notes: Source:
ISO 26262-4:2011, Clause 6.4.4
ISO 26262-4:2011, Clause 7.4.3.7
ISO 26262-4:2011, Clause 7.4.4.2
ISO 26262-4:2011, Clause 8.4.2.1.2
ISO 26262-6:2011, Clause 7.4.11
ISO 26262-6:2011, Clause 7.4.15
ISO 26262-6:2011, Clause 10.4.6

## Slide 34: Recommended Methods at Different ASIL
Notations for design | ASIL |  |  | 
 | A | B | C | D
Informal notations | ++ | ++ | + | +
Semi-formal notations | + | ++ | ++ | ++
Formal notations |  | + | + | +
Notations for design | ASIL |  |  | 
 | A | B | C | D
Informal notations | ++ | ++ | + | +
Semi-formal notations | + | ++ | ++ | ++
Formal notations |  | + | + | +
 | Neutral | + | Recommended
++ | Highly Recommended |  | 
 | Neutral | + | Recommended
++ | Highly Recommended |  | 
Notations for Software Architectural Design
Notes: Source:
- ISO 26262-6:2011, Clause 7.4.1

## Slide 35: Recommended Methods at Different ASIL
Methods for the verification of design | ASIL |  |  | 
 | A | B | C | D
Walkthrough | ++ | + |  | 
Inspection | + | ++ | ++ | ++
Prototype generation |  |  | + | ++
…… |  |  |  | 
Methods for the verification of design | ASIL |  |  | 
 | A | B | C | D
Walkthrough | ++ | + |  | 
Inspection | + | ++ | ++ | ++
Prototype generation |  |  | + | ++
…… |  |  |  | 
 | Neutral | + | Recommended
++ | Highly Recommended |  | 
 | Neutral | + | Recommended
++ | Highly Recommended |  | 
Methods for the verification of software architectural design
Notes: Source:
- ISO 26262-6:2011, Clause 7.4.18

## Slide 36: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 37: Further topics in ISO 26262
Standards on the management process
Hardware safety requirements and design
Standards on the post-release production phase
Configuration management
Change management
Qualification of HW/SW components and tools

## Slide 38: Outline
Why functional safety?
What is functional safety?
How is functional safety achieved for OS?
  Categorizing and controlling failures
  V-model development process
  Automotive Safety Integrity Level (ASIL)
Further topics
Conclusion

## Slide 39: Conclusion
Functional safety requires the control of failures and unintended behavior.
  Requirement, design and test phase verification to avoid unintended behavior
  Safety analysis to control systematic failures
  Safety mechanisms to control systematic and random failures
  Analysis of dependent failures to control dependent failures
Use ASIL to balance safety with cost.

## Slide 40: Thanks!