## Slide 1: Embracing the Terabyte Memory Era with Intel DCPMM In Cloud
董耀祖 (eddie.dong@intel.com)
首席工程师，Intel开源软件技术中心
Notes: 128GB, 192GB, 256GB, 384GB, 512GB….

## Slide 2: Computer Architecture Evolvement
CPU
Memory
（SRAM, DRAM)
Storage
CPU
Cache
(SRAM)
Storage
DDR
Core
L1
Storage
DDR
Core
L1
L2
Core
L1
Storage
HBM
Core
L1
L2
DDR
Core
L1
Storage
HBM
Core
L1
L2
DDR
DCPMM
（ Intel® Optane™ DC persistent memory）
Notes: L1: 3---5 cycles
L2: 10---22 cycles.
DDR: 300 cycles
HBM: DRAM堆叠技术

## Slide 3: Memory and Storage Sub-System in Cloud
MEMORY
Improving memory capacity
Improving SSD performance
Intel® 3D Nand SSD
STORAGE
DRAM
HDD/TAPE
SSD
Delivering efficient and scalable storage
Today’s Focus
Notes: DRAM: 20GB/s
DCPMM: >2X Optane GB/s
Opatne: 2-3GB/s better latency.
DRAM: NAND SSD -- -latency 1000X, BW: 1/10, capacity per $ = 40.
SSD: 2GB/s…
QLC SSD ; better latency
HDD: 200 MB/s

## Slide 4
Big and Affordable Memory
High Performance Storage
Direct Load/Store Access
128, 256, 512GB
High Reliability
Hardware Encryption
Supported on future Intel® Xeon® Scalable Processors (Cascade Lake)
DDR4 Pin Compatible
Native Persistence

## Slide 5: Intel® Optane™ DC Persistent Memory Hardware Interface
IMC
Intel® Xeon® Cascade Lake
IMC
DDR4 electrical and physical interface with proprietary protocol extensions
Memory channel can be shared between DDR4 and Intel® Optane™ DC persistent memory modules
    Enables systems to support greater than 3TB of system memory per CPU socket
Cache line size accesses
Idle latency close to DDR4 DIMMs
Intel® Optane™ DC Persistent Memory Module
Optimization Notice: Intel's compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit: http://www.intel.com/performance Source: Intel measured as of May 2018.
Performance measurements were obtained prior to implementation of recent software patches and firmware updates intended to address exploits referred to as "Spectre" and "Meltdown." Implementation of these updates may make these results inapplicable to your device or system.
Notes: DCPMM: 356ns
DDR:100ns
Optane: us

## Slide 6: Problem With Intel DCPMM
AppDirect (AD) Mode | Storage over AppDirect | ?
Memory | Block Device | Memory
Yes | No | No
Yes | Yes | No
Usage
App Change
Persistency
Customer Looking for app-transparent, high-perf memory solution
IaaS/VM renting
Commercial SW
TTM
“Others” owned SW

## Slide 7: PMEM as DRAM
NFIT Driver
VM1
vCPU
vCPU
vCPU
Memory
DRAM/PMEM
…
MemoryOptimizer
NFIT Driver
MemoryOptimizer
App
App
App
App
EPT
Page Table
Page Table
Page Table
Xeon
Xeon
CPU
DRAM
PMEM
Service Provider Software
End User Software
Xeon
Xeon
CPU
DRAM
PMEM
Hardware
App
App
App
VMn
vCPU
vCPU
vCPU
Memory
DRAM/PMEM
App
App
App
Hypervisor
(Linux)
Linux
Present homogeneous memory to VM
MemoryOptimizer: Map hot pages to DRAM thru EPT
VM
Usage
MemoryOptimizer: Map hot pages to DRAM thru OS Page table
Native Usage
End User Software

## Slide 8: Remap Hot Pages to DRAM
VM Usage
  Present PMEM and DRAM as homogeneous memory to guest VM
  MemoryOptimizer to migrate hot pages to DRAM
    Migrate guest pages to map hot pages to DRAM (cold pages to PMEM) thru EPT
Native Usage
  PMEM as normal memory, but in a separate NUMA node
  MemoryOptimizer to migrate hot pages to DRAM
    Migrate application pages to map hot pages to DRAM (cold pages to PMEM) thru OS page table

## Slide 9: MemoryOptimizer Architecture
Host Linux Kernel
KVM
Kernel
User
VM
Vanilla
Applications
Vanilla
Applications
Vanilla
Applications
EPT
Hotness Collector
Page
Migrator
PMU
Host Linux User
Actions
Policies (Per usage scenario)
Hotness Collector
Host Page Tables
MemoryOptimizer
Future Activity Predicators
Collectors

## Slide 10: MemoryOptimizer - Adaptive Policy Selection
Memory access pattern and predictors
  Access pattern is likely per workload
    Focus on typical cloud workload
  Need different predictors to handle different scenario
  Explore the possibility of AI in predictors
Usage scenario difference
  Throughput focus vs. latency focus
Policies
  Each predictor couldn’t precisely project the future page hotness
    Page mis-migration costs (actually pretty much for 2MB pages)
  Explore moderately conservative migration policy
    Avoid the cost of page mis-migration
    Workload and usage scenario specific

## Slide 11: Performance Evaluation
Amazing thing, Coming Soon!!!

## Slide 12: Summary
Terabyte memory era is rolling …
App-transparent memory solution, which features
  Good SLA control
  Cost effective
Intel is actively working on host side solution
Customer can innovate in migration algorithm and policy

## Slide 13: Backup – Original version